FUEL:

Use only PREMIUM GRADE 91 or higher octane fuel, which contains NO ALCOHOL.  Alcohol enhanced fuels rob your PWC of performance, and cause costly fuel system damage.

Fuel your PWC from a gas pump.  If you intend to use portable gas cans, be sure that the can is CLEAN, inside and out!  Even a few drops of water or a few grains of sand will adversely affect your performance and make repairs necessary.  Turn the fuel selector OFF when not in use!

OIL:

Use only PREMIUM GRADE oil, with appropriate specifications for your machine.  Ensure that the oil you use is intended for OIL INJECTED ENGINES.  We recommend Quicksilver, Sierra, or Sea-Doo Oils.  ALWAYS keep the oil tank FULL (add oil whenever you add fuel!)

CARE:

* Keep your machine well maintained.  If you experience performance problems, do not keep trying to run the machine.  Most system malfunctions will cause severe damage within minutes of their onset if not corrected.  We offer many services which can help you enjoy more fun in the sun:

* Spring Service (to catch up on needed repairs, lubrication, and tune-up)

* Winterization Service (to help prevent freezing/cracking of engine, souring of fuel, and internal engine rusting).  This procedure MUST be done before freezing weather each year REGARDLESS of where you store your machine.  Every year we see customers spend hundreds or even thousands of dollars on repairs that could have been avoided by proper winterization and lay-up.

*General Repairs (for performance problems that may develop).

* Stock Performance Solutions (to increase your PWC’s performance without sacrificing dependability).

DEBRIS:

Ensure that you NEVER start your PWC in less than 6 ft. deep water.  The jet pump on your PWC provides substantial suction under the machine, and will ingest any object on the bottom (or in the water) beneath the machine.  Do not operate your machine in debris-filled water.  Do not beach your PWC... rocks, sticks, etc. will lodge in the intake grate and be sucked into the pump on startup.  Following these instructions can save hundreds of dollars in costly pump repairs.

WATER INGESTION:

Water Ingestion is simply the entrance of water into the engine by some means.  It usually results in severe damage.  DO NOT attempt to start the engine if you suspect it has ingested water!  Common causes of water ingestion (which you should avoid) are:

- Launching without bilge plug

- Diving machine beneath surface (PWC’s are only water-tight BELOW the rub rail... anything above CAN AND WILL LEAK!)

- Overturn

- Towing machine

- Improper use of flush attachment (you should NEVER run water through the flush attachment unless the engine is RUNNING... turn water off and rev engine 2-3 times to blow water out when done!)

- Leaving machine unattended for more than 12 hours in water (pull it out when not in use.  Many machines are DESIGNED to leak a small amount of water to lubricate the driveshaft seal.

GET YOUR PWC IN FOR SERVICE WITHIN 12 HOURS IF YOU SUSPECT WATER INGESTION!

*** SEE REVERSE SIDE ***



How to SAVE MONEY with Proper Care of your PWC

17 Apopka Ave.

Greenville, SC  29609

(864)421-0444

Copyright 2003,European Marine

ENGINE STARTING:

Before starting your machine, check to ensure that there is no water in the bildge.  Next, you should:

1. Turn Fuel On

2. Apply FULL choke

3. Crank engine for no more than 15 seconds.

If engine fails to start, wait 30 seconds and repeat steps 2-3.

4.  After starting, you MUST allow the engine to warm-up at or near idle speed (no revving engine) for 60 seconds.  This will give engine time to reach operating temperature.  FAILURE TO ALLOW ADEQUATE WARM-UP WILL ALMOST CERTAINLY RESULT IN ENGINE FAILURE!

ELECTRONICS:

Do NOT attempt to disconnect, jump, or charge the battery in your PWC.  Your PWC is equipped with very sensitive electronic components which could be damaged easily.  Severe damage CAN, and OFTEN DOES result from:

- Battery Disconnection/Reconnection

- LOOSE battery connections

- Jump Starting

- Charging the Battery when in the

PWC.